## Slide 1
SMART INDIA HACKATHON 2026
Problem Statement ID – SIH26050
Problem Statement Title – High Altitude Performance Optimization and Robust Design of Anti-Drone System
Theme – Smart Automation / Security & Surveillance
PS Category – Hardware
Team ID – 165054
Team Name – WeAreDoomed
ACHAL a self-calibrating pointing head for high-altitude anti-drone systems

## Slide 2
WeAreDoomed
Team ID 165054
PROPOSED SOLUTION
At 4,500 m an anti-drone tracker doesn't fail loudly. It quietly misses.
ACHAL measures what the cold did to the machine and re-aims itself.
THE PROBLEM
Cold stiffens the machine
Cables, bearings & batteries derate
Sun & wind bend the aim
Thermal gradients + gusts at µrad scale
Calibration is frozen
Factory tables can't see what changed
The failure is silent
It keeps tracking while accuracy drops
ACHAL head
Drone (tracked)
Stars
Ridge
Marker
motor current = torque sensor
Fixed references the cold cannot move → the head re-fits its own aim
ACHAL IN 3 IDEAS
Torque fingerprint
Motor current split into friction, cable, imbalance, wind
Reference revisits
Markers, ridges & stars re-fit tilt, flexure, gyro bias, boresight
Capability gate
Declares live accuracy; engages only when GREEN
GREEN
AMBER
RED
WHERE IT SITS IN THE KILL CHAIN
Detect
wide camera
Track
2-axis gimbal
Identify
rotor signal + AI
Neutralize
effector handoff
ACHAL keeps every stage accurate in the cold

## Slide 3
WeAreDoomed
Team ID 165054
TECHNICAL APPROACH
1
SENSE THE EFFECTS
Motor & motion
current · encoders · IMU
Reference camera
markers · ridges · stars
Target sensing
wide camera · rotor photodiode
Environment
temp · pressure · humidity (priors)
2
BUILD THE SELF-MODEL
FAST · every cycle
Torque fingerprint
friction
cable
imbalance
wind
SLOW · every few min
Reference revisit
tilt
flexure
gyro bias
boresight
θ(t) ± σ
live self-model
RLS + Kalman + WLS
every estimate carries its uncertainty
3
CORRECT · JUDGE · DECLARE
Correct
ADRC + feedforward from the measured plant
Judge
inside cold-normal band → OK; outside → real fault
Declare
live jitter, ID range, confidence
VERIFY LOOP every revisit compares predicted accuracy with measured accuracy, then updates θ(t)
ACTUATION
BLDC direct drive · magnetic encoders · FOC
COMPUTE
Raspberry Pi 5 + real-time MCU
SENSING
IMU · 2 cameras · current · temp · photodiode
ESTIMATION
ADRC · RLS · Kalman · TPOINT model
VISION & AI
sub-pixel tracking · ONNX drone classifier
POWER
low-temp Li-ion · 3 heaters · health check

## Slide 4
WeAreDoomed
Team ID 165054
FEASIBILITY AND VIABILITY
PROTOTYPE BUILD COST
₹1.33 lakh
one complete prototype, including the −40 °C test bench
Pointing head ₹97k
Bench ₹29k
+5% contingency · itemised BOM in Budget Report
No radar · no FOG gyro · no GPU needed
WHY IT IS BUILDABLE
100% off-the-shelf
BLDC, encoders, Pi 5, MCU
Heat only 3 parts
battery · IMU · optical window
−40 °C campus bench
dry-ice box, fan, IR lamp, shaker
Proven maths
ADRC, RLS, Kalman, vision
BUILD ROADMAP
1
Physics proof
2
Gimbal head
3
Embedded sensing
4
Control stack
5
Cold & wind tests
6
Prediction check
7
Integration
8
Live A/B demo
TOP RISKS → HANDLED
Snow hides references
→ markers + ridges + stars; capability drops honestly
Frost / dust on optics
→ heated window + image-quality check
Cold battery
→ insulated heated pack, cold-charge lockout
Estimator drift
→ excitation gating, fallback to bench values

## Slide 5
WeAreDoomed
Team ID 165054
IMPACT AND BENEFITS
0
manual field recalibrations
references do the calibrating (design goal)
3
heated parts only
not the whole head, so power stays low
₹1.33 L
full prototype cost
incl. −40 °C bench, itemised BOM
WHAT CHANGES AT 4,500 M
TODAY · frozen calibration
WITH ACHAL
✕ Aim drifts in cold & wind
Aim held steady: identification range holds
✕ Technician must re-boresight
Boresight, tilt, gyro drift fixed in the field
✕ Cold looks like damage
Real faults (ice, slip, harness) flagged
✕ Fires blind on a bad aim
Operator sees live ID range; no blind engagement
WHO COULD USE IT
DRDO labs laser & EO trackers
BEL D4 / IDD&IS
Army Air Defence Ladakh, east
IAF high-altitude bases
ITBP / CAPF LAC posts
Critical infra Himalayan sites
potential users; no endorsement implied
Planet: low-power selective heating · People: safer, self-diagnosing operation · Profit: COTS, modular, scalable to DEW/EO trackers

## Slide 6
WeAreDoomed
Team ID 165054
RESEARCH AND REFERENCES
India already fields precision counter-drone systems (D4, IDD&IS, Mk-II(A) laser) [1–3]. Holding micro-radian aim at altitude is the open gap.
PUBLISHED TECHNIQUE → HOW ACHAL USES IT
Telescope pointing models
TPOINT [4]
→ re-fit from markers, ridges, stars
Disturbance observers
Springer 2020 [5]
→ ADRC on the measured plant gain
Gimbal torque calibration
US 7,437,222 [6]
→ done live in the field, not once in a lab
Auto-boresight
WO2000016152 [7]
→ checked by co-observing references
Jitter prediction
NASA survey [8]
→ run live to declare capability
Propeller signatures
EventRadar 2026 [9]
→ rotor photodiode for ID & kill check
Our novelty: each piece is published; the closed self-reference loop with live verification is ours.
SCAN TO SEE MORE
Live Simulation ↗
achal-simulation.vercel.app
Technical Report ↗
full ACHAL documentation
Budget Report ↗
itemised BOM + cost charts
1. BEL / DRDO. D4 Anti-Drone System.
2. Integrated Drone Detection & Interdiction System.
3. Business Standard. DRDO Mk-II(A) laser trial, Apr 2025.
4. P. Wallace. Telescope Pointing (TPOINT).
5. LOS stabilisation using a disturbance observer. Springer, 2020.
6. US 7,437,222. Gimbal disturbance calibration.
7. WO2000016152A1. Auto-alignment of EO elements.
8. NASA. Spacecraft line-of-sight jitter survey, 2020.
9. EventRadar: long-range UAV discovery. arXiv, 2026.
10. Adaptive servo control with LuGre friction. ASME JDSMC.
11. JSS 55555. Environmental tests for defence equipment.
12. Asian Military Review. MoD RFI, high-altitude C-UAS, 2026.