## Slide 1
SMART INDIA HACKATHON 2026
  Problem Statement ID – SIH26050
  Problem Statement Title- High Altitude Performance Optimization and Robust Design of Anti-Drone System
  Theme- Smart Automation / Security & Surveillance
  PS Category- Hardware
  Team ID- 165054
  Team Name - WeAreDoomed

## Slide 2
WeAreDoomed
Team ID 165054
PROPOSED SOLUTION
Problem at Hand
The cold changes the machine
Cables stiffen, bearings drag and sensors drift; motors, batteries and electronics derate.
Sun and wind bend and shake it
Thermal gradients and wind deform the structure and push the aim off target.
Calibration is frozen
Factory calibration and temperature-based compensation cannot see what actually changed.
The failure is silent
The system keeps tracking while its true pointing accuracy quietly degrades.
Our Solution ACHAL a self-referencing pointing head
Calibrate against what the cold cannot move
Instead of compensating for the weather, ACHAL measures what the weather did to the machine.
Drone: tracked
Ridge (far)
fixes azimuth
Marker (near)
fixes elevation
Stars (night)
high angles
ACHAL head
motor current
= torque sensor
sight line to a fixed reference
target track
Sense
effects
1
Torque
fingerprint
2
Aim
revisit
3
Model
θ(t) ± σ
4
Correct
ADRC
5
Judge
health
6
Declare
capability
7
Why We Stand Out
Measures the machine, not the weather
Calibrates against fixed references
Knows when it can't trust itself
motor current is split into named torques
friction
cable
imbalance
wind
markers
ridges
stars
re-fits the aim: encoder zero · tilt · flexure · gyro bias · boresight
cold-normal band
fault
GREEN
AMBER
RED
engages only when confident
Key Features
Torque fingerprint
Motor current reveals friction, cable stiffness, imbalance and wind
Reference revisits
Re-fit encoder offset, tilt, flexure, gyro bias and boresight
Live self-model θ(t)
Updated continuously, with its own uncertainty
Adaptive control
ADRC + feedforward from the measured plant
Cold vs broken
Health judged against cold-normal bands
Capability check
Predicts jitter, range and handoff; engages only when confident

## Slide 3
WeAreDoomed
Team ID 165054
TECHNICAL APPROACH
1 SENSE THE EFFECTS
2 BUILD THE SELF-MODEL
3 CORRECT · JUDGE · DECLARE
Motor & motion
motor current · encoders · IMU gyro
Reference imaging
narrow camera on markers, ridges, stars
Target sensing
wide camera (search) · rotor photodiode
Environment (priors only)
temperature · pressure · humidity
FAST
Torque fingerprint every control cycle
motor current
disturbance torque
RLS split
friction
cable
imbalance
plant gain
wind
SLOW
Reference revisit every few minutes
re-image references
sub-pixel offsets
WLS aim fit
encoder zero
tilt
flexure
gyro bias
boresight
one live self-model θ(t) ± σ via RLS + Kalman + WLS
θ(t)
Correct
ADRC + feedforward
FOC motor drives
direct-drive gimbal
pointing model, gyro bias and boresight applied to every command
Judge θ vs the cold-normal band at this temperature
inside band → cold, normal
outside band → fault
a fault is e.g. ice load, joint slip or harness damage
Declare jitter · handoff · ID range · confidence
GREEN
AMBER
RED
engagement gate → EO / laser payload interface
VERIFY every reference revisit compares the predicted accuracy with the measured one, then updates θ(t)
Environment
cold · wind · dust · snow
Sensing
cameras · IMU · encoders
Self-model
θ(t) + health
Adaptive control
ADRC + motor drives
Pointing
2-axis gimbal
Track & identify
camera + rotor signal
Stable aim output
EO / laser payload
Technology Stack
ACTUATION
• BLDC direct drive
• Magnetic encoders
• MCU + FOC
• Aluminium frame
COMPUTE
• Raspberry Pi 5
• MCU real-time loops
• Local display + logs
• 4G / Wi-Fi link
SENSING
• IMU + cameras
• Current + temperature
• Pressure + humidity
• Rotor photodiode
CONTROL & ESTIMATION
• ADRC control
• RLS torque ID
• Kalman + WLS
VISION & AI
• TPOINT aim model
• Sub-pixel tracking
• ONNX drone classifier
POWER & HEALTH
• Low-temp Li-ion pack
• 3 selective heaters
• DC-DC power mgmt
• Health + capability check

## Slide 4
WeAreDoomed
Team ID 165054
FEASIBILITY AND VIABILITY
Why It Is Feasible
Prototype Build Cost
Off-the-shelf parts
BLDC motors, encoders, Pi 5 and MCU are all COTS
No radar, laser or GPU
the method proves itself without them
Pi 5 + MCU
vision on the Pi, real-time loops on the MCU
Heat only 3 parts
battery, IMU and optical window
−40 °C campus bench
dry-ice box, fan, IR lamp and shaker
Proven methods
ADRC, RLS, Kalman and vision
≈ ₹1.33 lakh one prototype incl. test bench
Pointing head
Bench
≈ ₹97k
≈ ₹29k
Avoided by design
FOG gyro
heated head
event camera
GPU
itemised BOM + 5% contingency · see Budget Report
How We Actually Build It
1
Physics proof
cold-box curves: cable, friction, drift
2
Mechanical head
2-axis direct-drive gimbal
3
Embedded sensing
FOC, current sense, timestamps
4
Control stack
ADRC, RLS, revisit fit
5
Cold & wind tests
−40 °C, wind, vibration
6
Prediction check
predicted vs measured
7
Integration
cue → track → ID → gate
8
Final demo
live A/B in the cold box
Key Risks and How We Handle Them
RISK
WHAT IT WOULD CAUSE
HOW WE HANDLE IT
µrad accuracy is hard
a small angle error is a big miss at range
sub-pixel tracking and optical-lever checks; validated at −40 °C, wind, vibration
Snow or cloud hides references
aim drift goes unmeasured
markers + terrain + stars; uncertainty grows, so the declared capability drops
Estimator drift
wrong compensation at low excitation
excitation gating and bounded estimates; fall back to bench values
Frost or dust on optics
blurred view, shorter ID range
heated window; image-quality check on reference textures
Cold battery
brownouts, short endurance
insulated heated pack; cold-charge lockout
Revisit leaves the sector
brief gap in watch
revisits are interruptible and run when idle

## Slide 5
WeAreDoomed
Team ID 165054
IMPACT AND BENEFITS
0
Manual field recalibrations
markers, ridges and stars do the calibrating (design goal)
3
Heated parts only
battery · IMU · window, not the whole head, so power stays low
₹1.33 L
Prototype build cost
including the −40 °C test bench (itemised BOM estimate)
Who Could Use It
DRDO labs laser DEW and EO trackers
BEL D4 / IDD&IS production
Army Air Defence Ladakh and eastern sector
IAF high-altitude airfields
ITBP / CAPF posts on the LAC
Critical infrastructure Himalayan sites
potential users, no endorsement implied
Immediate Impact
CAPABILITY
WHAT CHANGES ON THE GROUND
WHY IT MATTERS
Torque fingerprint + ADRC
Aim stays steady in cold and wind
so identification range holds
OPERATIONAL
range preserved
Reference revisits
Boresight, tilt, gyro drift fixed in the field
with no technician visit
LOGISTICS
fewer field visits
Cold-normal health
Cold no longer looks like damage
real faults (ice, slip, harness) flagged
RELIABILITY
the right alarms
Capability gate
Operator sees the live ID range
no engagement while aim is uncertain
SAFETY
no blind engagement
Long-Term Value
PLANET
Low-power thermal design · selective heating · reusable hardware · reduced energy use
PEOPLE
Reliable tracking · minimal manual calibration · safer operation · self-diagnostics
PROFIT
Low-cost prototype · COTS components · modular maintenance · scalable defence integration

## Slide 6
WeAreDoomed
Team ID 165054
RESEARCH AND REFERENCES
Research what is already published, what it proves, and where it lives in ACHAL
Precision counter-drone systems already exist in India: D4 (DRDO + BEL), IDD&IS and the Mk-II(A) laser weapon [1–3]. Laser engagement needs micro-radian pointing; holding it at altitude is the open gap.
Telescope pointing models
Star sightings fit a pointing model with thermal and flexure terms.
In ACHAL: the same model, re-fit from markers, ridges and stars
TPOINT, Wallace [4]
Disturbance observers
Estimating disturbance torque stabilises the line of sight.
In ACHAL: ADRC rate loop using the plant gain we measure
Springer, 2020 [5]
Gimbal torque calibration
Harness stiffness and friction can be measured and compensated.
In ACHAL: done continuously in the field, not once in a lab
US 7,437,222 [6]
Auto-boresight
Laser-to-sensor alignment drifts with temperature.
In ACHAL: boresight checked by co-observing the references
WO2000016152 [7]
Jitter prediction
Disturbance spectrum × system response predicts jitter.
In ACHAL: run live to declare capability
NASA jitter survey [8]
Propeller signatures
Drones identified by blade periodicity at 0.7–1.5 km.
In ACHAL: rotor photodiode for ID and kill check
EventRadar, 2026 [9]
Our integration, ACHAL
Sense
Torque
Revisit
θ(t)
Correct
Judge
Declare
Verify
Each technique is published; the self-reference loop and its verification are ours.
References
1. BEL / DRDO. D4 Anti-Drone System.
2. Integrated Drone Detection & Interdiction System (IDD&IS).
3. Business Standard. DRDO Mk-II(A) laser weapon trial, Kurnool, Apr 2025.
4. P. Wallace. Telescope Pointing (TPOINT).
5. Line-of-sight stabilisation using a disturbance observer. Springer, 2020.
6. US 7,437,222. Gimbal disturbance calibration and compensation.
7. WO2000016152A1. Automatic alignment and stabilisation of electro-optical elements.
8. NASA. A survey of the spacecraft line-of-sight jitter problem, 2020.
9. EventRadar: long-range UAV discovery through event sensing. arXiv, 2026.
10. Adaptive control of servo systems with LuGre friction. ASME JDSMC.
11. JSS 55555. Environmental test methods for defence equipment.
12. Asian Military Review. MoD RFI for high-altitude counter-drone systems, 2026.
Links
1
Documentation
Complete ACHAL technical report
↗
2
Budget Report
Detailed BOM + cost analysis + charts
↗
3
Prototype Simulation
Interactive ACHAL web demo
↗
4
Simulation Demo
Recorded walkthrough video
↗